## Slide 1: Consensus Equilibrium for Super-Resolution and Extreme-Scale CT Reconstruction
Xiao Wang1, Venkatesh Sridhar2, Zahra Ronaghi3, Rollin Thomas3, Jack Deslippe3, Dilworth Parkinson3, Gregery Buzzard2, Samuel Midkiff2, Charles Bouman2, Simon Warfield1
1Harvard Medical School, Boston Children’s Hospital
2Purdue University
3Berkeley National Lab

## Slide 2: Computed Tomography (CT) Reconstruction
Parallel X-ray Source
Parallel X-ray Source
Parallel X-ray Source
Parallel X-ray Source
Reconstruction
Detector
Detector
Detector
Detector
row
channel

## Slide 3: Tomographic Reconstruction
X-rays
X-ray Detector
Sample Slice
Sample Object
measurements
X-ray Source
voxel
Medical CT scanners
Synchrotron Imaging
Electron Microscopy
single measurement
voxel
voxel
voxel
rotation axis

## Slide 4: Two Approaches for Reconstruction
Filtered-back Projection (FBP)
Fourier transform and inverse Fourier transform
Feldkamp (FDK) Algorithm, Siemens ADMIRE, GE ASiR and etc. (clinical-standard IR)
advantage: light-weight, easy to implement
disadvantage: loss of resolution, and more image artifacts
Model Based Iterative Reconstruction (MBIR)
  Physics-geometry forward model
  Image spatial property prior model
  Linear algebra and Bayesian estimation
  advantage: higher spatial resolution, fewer artifacts
  disadvantage: complexity, computation time, memory requirement

## Slide 5: Model Based Iterative Reconstruction (MBIR)
traditional reconstruction (FBP)
MBIR reconstruction
¼ the X-ray dosage!

## Slide 6
Siemens ADMIRE
MBIR

## Slide 7
Detector
X-ray Source
X-ray
voxels
channels
channels
X-ray
X-ray Source
(b)
rows
channels
X-ray Source
X-ray
(c)
rows
rows

## Slide 8
measurements vector
system matrix
Reconstruction vector
error vector
Issues:
(1) large system matrix.
(2) error, , is unknown and cannot be measured.
(3) For super-resolution reconstruction, reconstruction is undetermined with many solutions.

## Slide 9: MBIR Cost Function
Can be understood as a machine learning problem.
Issues:
    System matrix, , is too large for storage in any computer memory. Partition it is not easy.
    Parallelism focuses on partitioning reconstruction, .
weight matrix
voxel xj
26 voxels local neighborhood

## Slide 10: MBIR Good Performance
New parallelism that partitions measurements, , and also reconstruction, , with guaranteed convergence.
Partition the system matrix, , across nodes, without corrupting its information.
Achieves both goals through the Consensus Equilibrium (CE) Method.

## Slide 11: Contributions
For super-resolution CT reconstruction, the Asynchronous Consensus MBIR (AC-MBIR) has :
6.8 times smaller memory footprint
16 times more scalability, compared with the state-of-the-art MBIR implementation
maintains a 100% strong scaling efficiency at 146880 cores.
In addition, AC-MBIR achieves an average bandwidth of 3.5 petabytes per second at 587520 cores.

## Slide 12: The Consensus Equilibrium Method (CE Method)
reconstruct
reconstruct
reconstruct
High-resolution consensus solution,
Fuse
Repeat
In any order
“Magical” Merge
Note: Consensus solution, , equals the global minimum of MBIR cost function.

## Slide 13: Low-Resolution Individual Reconstruction
Individual reconstruction
measurement subset
system matrix subset
is the number of subsets
is a convergence parameter
consensus solution

## Slide 14: Uniform View Subsets
Parallel X-ray Source
Parallel X-ray Source
Parallel X-ray Source
Parallel X-ray Source
Reconstruction
Detector
Detector
Detector
Detector

## Slide 15: Grouped View Subsets
Parallel X-ray Source
Parallel X-ray Source
Parallel X-ray Source
Parallel X-ray Source
Reconstruction
Detector
Detector
Detector
Detector

## Slide 16: Smaller Memory Footprint with Grouped-View Subsets
measurements for an SV
view angles
channels
rows
block1
block2
subset 1
block1
block2
subset 2
block1
block2
subset 1
block1
block2
subset 2
SV
reconstruction
voxels
uniform view subsets
grouped view subsets

## Slide 17
sub-volume
sub-volume
sub-volume
sub-volume
sub-volume
sub-volume
sub-volume
sub-volume
individual reconstruction,
individual reconstruction,
sub-volume
sub-volume
sub-volume
sub-volume
consensus solution,
and
and
and
and
Broadcast & Merge
Broadcast & Merge
Parallelism
Achieves measurement-partition parallelism and reconstruction volume partition at the same time.
cluster
cabinet

## Slide 18
FBP interpolation method
The same area by MBIR
Super-Resolution Benchmark Dataset
Ceramic matrix composite dataset, containing 2366 slices from Berkeley Lab Advanced Photon Source.

## Slide 19: Benchmark Dataset
Dataset:
  Measurement size: 2560 channels; 2366 rows, 1024 views; parallel view
  Reconstruction size is 3600 x 3600 x 2366
  Processors:
  NERSC supercomputer from Berkeley National Lab (knights landing clusters)
  Each node: 68 cores Intel processors

## Slide 20
Grouped-view subsets (uniform view subsets) | 1 | 2 | 4 | 8 | 16
Nodes | 108 | 216 | 432 | 864 | 1728
Memory footprint per node (GB) | 58 (58) | 31 (33) | 18 (21) | 11 (15) | 8 (11)
Memory reduction | 1x (1x) | 1.8x (1.7x) | 3.2x (2.7x) | 5.2x (3.9x) | 6.8x (5.1x)
Runtime (seconds) | 1681 (1681) | 779 (807) | 342 (385) | 258 (347) | 215 (347)
Computation Increase | 1 (1) | 1 (1) | 1 (1.2) | 1.1 (1.5) | 1.3 (2.1)
Parallel efficiency | 100% (100%) | 108% (104%) | 123% (131%) | 89% (91%) | 63% (63%)
Bandwidth (petabytes/ sec) | <0.1 (<0.1) |  |  |  | 

## Slide 21
Number of Sub-volumes (4 view subsets) | 68 | 135 | 270 | 540 | 1080 | 2160
Nodes | 272 | 540 | 1080 | 2160 | 4320 | 8640
Memory footprint per node (GB) | 20 (23.7) | 17.4 (20.4) | 15.7 (18.7) | 14.9 (17.9) | 14.5 (17.5) | 14.3 (17.30)
Memory reduction | 2.8x (2.4x) | 3.3x (2.8x) | 3.7x (3.1x) | 3.9x (3.2x) | 4.0x (3.3x) | 4.1x (3.4x)
Runtime (seconds) | 558.0 (654.6) | 271 (326.4) | 147.2 (174.3) | 84.4 (159.2) | 51.4 (154.0) | 40.0 (154.0)
Computation Increase | 1 (1.2) | 1 (1.2) | 1 (1.2) | 1 (1.2) | 1 (1.2) | 
Parallel efficiency | 120% (122%) | 124% (124%) | 114% (116%) | 100% (63%) | 82% (33%) | 53% (16%)
Bandwidth (petabytes/ sec) | <0.1 (<0.1) | <0.1 (<0.1) | 0.1 (0.1) | 0.4 (0.3) | 1.4 (0.5) | 3.5 (1.1)

## Slide 22
Chart: Full Iterations
Grouped View Subsets Convergence