## Slide 1: Topology-Custom UGAL Routing on Dragonfly
  Shafayat Rahman
  Saptarshi Bhowmik
  Yevgeniy Ryasnianskiy
  Xin Yuan
  Michael Lang

## Slide 2: Contributions
Dragonfly is a dominant topology in HPC, and UGAL is the preferred routing
We showed: the performance of UGAL can be significantly improved on many instances of DF, specially the ones that have “smaller” number of groups, by customizing the set of paths in UGAL
We call this improved version of UGAL as Topology-Custom UGAL (T-UGAL)
Notes: Cray Cascade architecture, deployed in Trinity in Los Alamos, and Titan in Oak Ridge.
Cray Slingshot architecture also uses DF, which is for future.

## Slide 3: Contributions
We developed a multi-step scheme to compute the custom set to non-minimal paths for a given topology
We showed that T-UGAL offers significant performance improvement over conventional UGAL on many DF topologies
Notes: Cray Cascade architecture, deployed in Trinity in Los Alamos, and Titan in Oak Ridge.
Cray Slingshot architecture also uses DF, which is for future.

## Slide 4: Dragonfly Topology
Notes: In real life, its possible to have
: variable number of groups
: variable number of global links between groups
For example, full-sized DF has only one global link between the groups. But Cray Cascade has multiple (four, or two in some cases).

## Slide 5: Dragonfly

## Slide 6: Minimal Routing in Dragonfly
S
D

## Slide 7: Non-Minimal (VLB) Routing in Dragonfly
S
D
I1

## Slide 8: Non-Minimal (VLB) Routing in Dragonfly
S
D
I1
I2

## Slide 9: Adaptive (UGAL-L) Routing in Dragonfly
S
D
I1

## Slide 10: Adaptive (UGAL-L) Routing in Dragonfly
S
D
I1

## Slide 11: Adaptive (UGAL-L) Routing in Dragonfly
S
D
I1

## Slide 12: Routing in Dragonfly
The method to decide VLB paths in UGAL does NOT adapt to the network topology.
The question is: are ALL the VLB paths in DF are absolutely necessary to achieve sufficient path diversity?
Notes: There exists many 3, 4 and 5 hops VLB paths along with the regular 6-hop paths.

## Slide 13: Intuition
In many practical instances of Dragonfly, the number of groups is less than the theoretical maximum for that configuration
This may lead to more than one global links between the groups
More global links between groups lead to:
  More than one minimal path between s-d pairs
  More variations in VLB paths lengths
Notes: There exists many 3, 4 and 5 hops VLB paths along with the regular 6-hop paths.

## Slide 14: Intuition

## Slide 15: Intuition

## Slide 16: Intuition
S
D
I
Notes: Traditional 6 hop path

## Slide 17: Intuition
Notes: 5 hop paths

## Slide 18: Intuition
Notes: 4 hop paths

## Slide 19: Intuition
It might be possible to use only the shorter non-minimal paths, and achieve sufficient path-diversity even for the adversarial traffic patterns
Using shorter paths leads to less resource consumption, and may lead to overall improvement in performance
Notes: Can we provide a table here with the percentage of smaller paths in a certain DF topology?

## Slide 20: Intuition
We try to find a set of VLB paths for each DF topology that:
  Reduces the average path length
  And provides sufficient path-diversity for any adversarial traffic pattern
Once found, we restrict UGAL to select non-minimal paths from only this set

## Slide 21: Challenge
How to ensure “sufficient” path diversity?

## Slide 22: Challenge
How to ensure “sufficient” path diversity?
We know the most demanding traffic pattern for Dragonfly: Adversarial Shift.

## Slide 23: Shift Traffic Pattern in DF

## Slide 24: Shift Traffic Pattern in DF

## Slide 25: Shift Traffic Pattern in DF

## Slide 26: Shift Traffic Pattern in DF

## Slide 27: Shift Traffic Pattern in DF

## Slide 28: Shift Traffic Pattern in DF
An adversarial shift pattern quickly consumes all the available b/w on the direct links between two group
This will force UGAL to switch to VLB paths
If T-UGAL can support such patterns (better than, or at least as good as UGAL), it is reasonable to assume that it will handle any other non-adversarial pattern.

## Slide 29: T-UGAL: Properties
T-UGAL has the same routing mechanism as in UGAL
T-UGAL uses the same set of minimal paths as in UGAL
T-UGAL uses a subset of VLB (non-minimal) paths used in UGAL
  The set of paths (T-VLB) is customized for the underlying topology
  Has an average path length of as small as possible

## Slide 30: Computing T-VLB: Steps
Identify of the most demanding traffic patterns for DF
Initialize candidate T-VLB path sets.
Perform a coarse-grain performance estimation of T-VLB candidate path sets.
  Choose the top-performing ones as the interim candidate sets.
Consider augmenting the interim candidate pool with strategic choices

## Slide 31: Computing T-VLB: Steps
For each interim candidate set:
  Perform load-balance analysis
  Perform load-balance adjustments
Evaluate the adjusted candidates through simulation.
  Choose the highest performing candidate set as the final path set.

## Slide 32: Step 1: Identify the Most Demanding Traffic Patterns
We consider two types of adversarial shift traffic patterns
  Type-1 Set: Deterministic
  Type-II Set: Non-deterministic

## Slide 33: Type-I Sets

## Slide 34: Type-I Sets

## Slide 35: Type-I Sets

## Slide 36: Type-I Sets

## Slide 37: Type-I Sets

## Slide 38: Type-I Sets
Notes: Shift by (1,0) => 1 group, 0 router.

## Slide 39: Type-I Sets

## Slide 40: Type-I Sets

## Slide 41: Type-I Sets

## Slide 42: Type-I Sets

## Slide 43: Type-I Sets
Each group shifts to one other group
Additionally, nodes in the source group can also shift in a specific way to nodes in the destination group
(g-1)*a number of possible patterns

## Slide 44: Type-II Sets

## Slide 45: Type-II Sets

## Slide 46: Type-II Sets

## Slide 47: Type-II Sets

## Slide 48: Type-II Sets

## Slide 49: Type-II Sets

## Slide 50: Type-II Sets

## Slide 51: Type-II Sets
Type-2 Set:
  A random permutation is done at group level
  For each group pair, a router level permutation is done
  Virtually unlimited number of such permutations are possible.
We consider 20 of them, randomly picked.
Notes: Any other pattern will be more “uniform” in comparison to these
So they should be possible to be handled at least as effectively as UGAL.

## Slide 52: Step II: Coarse-grain Performance Estimation
Starts with many candidate VLB path subsets
Uses a performance model to estimate the potential throughput of the candidate VLB path subsets, for each traffic pattern selected
Chooses the ones with best estimated performance as interim candidates

## Slide 53: Step II: Coarse-grain Performance Estimation
The performance estimation model used is a modified version of model 3 proposed by Mollah et al.
It is quite accurate and efficient
* Md Atiqul Mollah et al., "Modeling UGAL on the Dragonfly Topology," the SC17 workshop on Performance Modeling, Benchmarking and Simulation of High Performance Computer Systems (PMBS17), Denver, Co, November 11, 2017

## Slide 54: Step II: Coarse-grain Performance Estimation

## Slide 55: Step II: Coarse-grain Performance Estimation
Notation | Explanation
3-hop paths | All paths 3-hop or less
10% 4-hop paths | All paths 3-hop or less, plus 10% 4-hop paths
… | …
90% 4-hop paths | All paths 3-hop or less, plus 90% 4-hop paths
4-hop paths | All paths 4-hop or less
10% 5-hop paths | All paths 4-hop or less, plus 10% 5-hop paths
… | …
90% 5-hop paths | All paths 4-hop or less, plus 90% 5-hop paths
5-hop paths | All paths 5-hop or less
10% 6-hop paths | All paths 5-hop or less, plus 10% 6-hop paths
… | …
90% 6-hop paths | All paths 5-hop or less, plus 90% 6-hop paths
6-hop paths | All paths 6-hop or less
Notes: For each of the points, we collect model performance of type_1 and type_2 set traffic patterns.
We take their average.
We select the points that give the best performance prediction + some more points in its vicinity. These will be the inputs in Step 3.

## Slide 56: Step II: Coarse-grain Performance Estimation
Notes: dfly(4,8,4,9) network
interim candidate sets: 40%, 50%, 60% and 70%

## Slide 57: Step II: Coarse-grain Performance Estimation
Notes: dfly(4,8,4,9) network
interim candidate sets: 40%, 50%, 60% and 70%

## Slide 58: Step II: Coarse-grain Performance Estimation
Notes: dfly(4,8,4,33) network

## Slide 59: Step III: Interim candidate set augmentation and analysis
We may add some deterministic “strategic choice” path sets
  We were randomly selecting x% of n-hop links before
  However, sometimes deterministically selection the paths may lead to better load-balancing
We considered two deterministic 50% 5-hop sets.
Notes: So for our example dfly(4,8,4,9) network, we considered six candidate sets: 40%, 50%, 60% and 70% random 5-hop paths, plus two deterministic strategic choices.

## Slide 60: Deterministic Strategic Choice: 1
Sets of paths with 2-hop min paths followed by 3-hop min paths
I
D
S
S
I
D
Notes: 4 hop paths

## Slide 61: Deterministic Strategic Choice: 1I
Sets of paths with 3-hop min paths followed by 2-hop min paths
S
I
D
S
I
D
Notes: 4 hop paths

## Slide 62: Step III: Interim candidate set augmentation and analysis
For each interim candidate set:
  Perform load-balance analysis
  Perform load-balance adjustments
Notes: Load-balance analysis is need for T-UGAL because some T-UGAL does not use all the paths. So this may lead to overusing of some links.
We perform load-balance analysis by calculating link-usage analysis for all the links with the assumption that:
Each candidate VLB path is equally likely to be taken by a packet between an SD pair
A packet is equally likely to be between any SD pair
We perform load-balance adjustments by removing over-used paths. (Could take more sophisticated approach, but it works, so why bother?)

## Slide 63: Step IV: Simulation
Finalize T-VLB through simulation.
Notes: Simulation is done for adversarial traffic and highest performing candidate set is chosen finally.
The selection is validated with:
Different version of UGAL
Different traffic patterns

## Slide 64: Deterministic Strategic Choice: 1
Sets of paths with 2-hop min paths followed by 3-hop min paths
I
D
S
S
I
D
Notes: 4 hop paths

## Slide 65: Step IV: Simulation
Finalize T-VLB through simulation.
Notes: Simulation is done for adversarial traffic and highest performing candidate set is chosen finally.
The selection is validated with:
Different version of UGAL
Different traffic patterns

## Slide 66: Step IV: Simulation
Finalize T-VLB through simulation.
Notes: Simulation is done for adversarial traffic and highest performing candidate set is chosen finally.
The selection is validated with:
Different version of UGAL
Different traffic patterns

## Slide 67: Performance Study
Performance of T-UGAL was analyzed and validated through simulation
Varying parameters:
  Dragonfly topology
  Adaptive routing scheme
  Traffic pattern

## Slide 68: Dragonfly Topology
Topology | No. of PEs | No. of switches | No. of groups | Links per group pair
dfly(4,8,4,33) | 1056 | 264 | 33 | 1
dfly(4,8,4,17) | 544 | 135 | 17 | 2
dfly(4,8,4,9) | 288 | 72 | 9 | 4
dfly(13,26,13,27) | 9126 | 702 | 27 | 13
Notes: DF topologies used in the experiments

## Slide 69: Adaptive Routing Schemes
Existing Routing Scheme | Upgraded Routing Scheme
UGAL-L | T-UGAL-L
UGAL-G | T-UGAL-G
PAR | T-PAR
Notes: Routing Schemes Considered

## Slide 70: Traffic Patterns
Traffic Patterns
Adversarial Shift
Uniform Random
Random Permutation
Shift + Uniform mixed (Space-domain)
Shift + Uniform mixed (Time-domain)

## Slide 71: Booksim 2.0
Parameter | Value
No. of virtual channels | 4 for UGAL-L and UGAL-G 5 for PAR
Buffer size | 32
Link latency | 10 cycles (local) 15 cycles (global)
Router internal speedup | 2
Notes: Simulator settings

## Slide 72: Shift(2,0), df(4,8,4,9)
Notes: Shift pattern shift by (2,0), a 8 g 9

## Slide 73: Random Permutation, df(4,8,4,9)
Notes: Rperm, a 8 g 9

## Slide 74: Shift+Uniform Mixed (Space Domain), df(4,8,4,17)
Notes: PE-based shift-uniform. 25% shift, vs 75% shift. A8 g 17.

## Slide 75: Shift+Uniform Mixed (Time Domain), df(4,8,4,17)
Notes: Time-based shift-uniform. 50% shift. A8 g 17.

## Slide 76: df(13,26,13,27)
Notes: Large network. A26 g27. Shift by 1 group, vs Pe-based Mixed(50% shift)

## Slide 77: Summary: T-UGAL in Dragonfly
We proposed T-UGAL routing for Dragonfly
We developed a general scheme for any DF topology to obtain the set of VLB paths, T-VLB, to be used in T-UGAL
We demonstrated that T-UGAL achieves significant performance improvement over UGAL for a broad range of DF topologies